## Slide 1: District One Advanced Traffic Safety Academy
Presented by: Larry Hagen, P.E., PTOE, RSP
Session 4 – Advanced Signalized
Intersection Safety Treatments

## Slide 2: Advanced Traffic Safety Academy
Florida’s SHSP Update
NCHRP 500
Combining Safety Countermeasures
Advanced Signalized Intersection Safety Treatments
Hot-Button Safety Review
Innovative Intersection Designs
Human Factors in Highway Safety
Safety Evaluation Workshop
Advanced Unsignalized Intersection Safety Treatments
Safe Systems Approach
Safety Evaluation Workshop
Building a Safety Culture

## Slide 3: Advanced Traffic Safety Academy
Florida’s SHSP Update
NCHRP 500
Combining Safety Countermeasures
Advanced Signalized Intersection Safety Treatments
Hot-Button Safety Review
Innovative Intersection Designs
Human Factors in Highway Safety
Safety Evaluation Workshop
Advanced Unsignalized Intersection Safety Treatments
Safe Systems Approach
Safety Evaluation Workshop
Building a Safety Culture

## Slide 4: Signalized Intersection Safety
What can we do to make our signalized intersections safer?

## Slide 5: NCHRP 500 Series
Volume 12: A Guide for Reducing Collisions at Signalized Intersections
Notes: My main reference for today’s session.

## Slide 6: Fatal Crashes by relationship to junction
Source: 2002 FARS

## Slide 7: 2002 FARS Data:
23 percent of all fatal crashes occurred at intersections,
6 percent of all fatal crashes occurred at signalized intersections,
29 percent of fatal crashes at intersections occurred at signalized intersections,
84 percent of fatal crashes at signalized intersections occurred in urban areas, and
59 percent of fatal crashes at signalized intersections involve angle collisions with other vehicles.

## Slide 9: Objectives of This Emphasis Area
Reduce frequency and severity of intersection conflicts through traffic control and operational improvements
Reduce frequency and severity of intersection conflicts through geometric improvements
Improve sight distance at signalized intersections
Improve driver awareness of intersections and signal control
Improve driver compliance with traffic control devices
Improve access management near signalized intersections
Improve safety through other infrastructure treatments

## Slide 10
Notes: P = proven; T = Tried; E = experimental

## Slide 14: Questions?

## Slide 15: Signalized Intersection Safety
Can we get some more details on these countermeasures?
Notes: You may have asked yourself this question…the answer is YES!

## Slide 16: Category A – Reduce Frequency and Severity of Intersection Conflicts through Traffic Control Improvements

## Slide 17: A1 – Employ Multiphase Signal Operation
This strategy includes using protected left-turn phases and split phases.
A two-phase signal is the simplest method for operating a traffic signal, but multiple phases may be employed to improve intersection safety.
Left turns are widely recognized as the highest-risk movements at signalized intersections. Protected left-turn phases significantly improve the safety for left-turn maneuvers by removing conflicts with the left turn.
Split phases, which provide individual phases for opposing approaches may also increase the overall delay experienced at an intersection. However, this strategy may improve intersection safety.
Notes: LOTS of good information and references in the NCHRP 500 report about how and why to consider protected left turns.

## Slide 18: A2: Optimize Clearance Intervals
The clearance interval is the portion of a signal cycle between the end of a green phase and the beginning of the next green phase for a conflicting movement. Clearance times provide safe, orderly transitions in ROW assignment between conflicting streams of traffic. The clearance interval can include both yellow and all-red time between conflicting green phases.
Notes: An important thing to know and understand here: NCHRP 500 here uses a different definition than the MUTCD. In the MUTCD, the yellow is the change interval, and the all-red is the clearance interval.

## Slide 19: A3: Restrict or Eliminate Turning Maneuvers
Safety at some signalized intersections can be enhanced by restricting or prohibiting turning maneuvers, particularly left turns. This strategy can be applied during certain periods of the day (such as peak traffic periods) or by prohibiting particular turning movements altogether. This strategy may be appropriate where a turning movement is considered to be “high risk” and other strategies (such as left-turn channelization or retiming of signals) are impractical or not possible to implement.
Notes: This strategy includes restricting or eliminating left- or right-turning maneuvers using channelization or signing and prohibiting right turns on red (RTOR).
Some agencies do skip protected left turns or only do protected left turns by time of day.

## Slide 20
Restrict or Eliminate Turning Maneuvers Using Channelization or Signing. Turn restrictions and prohibitions can be implemented by channelization or signing. Raised concrete channelization or flexible delineators can be used to physically prevent drivers from making restricted maneuvers. Turning prohibitions or restrictions implemented with signing alone will most likely require some periodic enforcement. The cost of enforcement should be considered when discussing methods for restricting or prohibiting turns.
A3: Restrict or Eliminate Turning Maneuvers (cont.)

## Slide 21: A3: Restrict or Eliminate Turning Maneuvers (cont.)
Prohibit Right Turns on Red. Prohibition of RTOR can help reduce crashes related to limited sight distance and pedestrians that involve right-turning vehicles. This strategy can also help reduce the frequency and severity of crashes between vehicles turning right on red and vehicles approaching from the left on the cross street or turning left from the opposing approach. Prohibition of RTOR may also be a safety-effective strategy where weaving or other conflicts are evident downstream of the right turn. Prohibition of RTOR at specific intersections can be implemented during certain times of the day (such as when pedestrians are more likely to be present).

## Slide 22: A4: Employ Signal Coordination
Signal coordination has long been recognized as having beneficial effects on the quality of traffic flow along a street or arterial. Good signal coordination can also generate measurable safety benefits, primarily in two ways:
Coordinated signals produce platoons of vehicles that can proceed without stopping at multiple signalized intersections. Reducing the number and frequency of required stops and maintaining constant speeds for all vehicles reduces rear-end conflicts.
Signal coordination can improve the operation of turning movements.
Notes: [bullet 2] Drivers may have difficulty making permitted turning maneuvers at signalized intersections (e.g., permitted left turns, RTOR after stop) because of lack of gaps in through traffic. Crashes may occur when drivers become impatient and accept a gap that is smaller than needed to complete a safe maneuver. Such crashes could be reduced if longer gaps were made available.
Increased platooning can create more gaps of increased length for permitted vehicle movements at intersections and result in improved intersection operation.

## Slide 23: A5: Employ Emergency Vehicle Preemption
Signal preemption allows emergency vehicles to disrupt a normal signal cycle in order to proceed through the intersection more quickly and under safer conditions. The preemption systems can extend the green on an emergency vehicle’s approach or replace the phases and timing for the whole cycle. The MUTCD discusses signal preemption, standards for the phases during preemption, and priorities for different vehicle types that might have preemption capabilities.

## Slide 24: A6: Improve Operation of Pedestrian and Bicycle Facilities
Traffic control improvements that can be made to an intersection to increase pedestrian safety include the following:
Pedestrian signs, signals, and markings,
Crossing guards for school children,
Lights in crosswalks in school zones,
Pedestrian-only phase or LPI during signal operation,
Prohibition of RTOR,
Technology to show a push button is working (i.e. LED confirmation)

## Slide 25: A7: Remove Unwarranted Signal
Traffic signals can remedy many safety and operational problems at intersections. However, signals often can adversely affect intersections. It is possible that a signal may no longer be warranted due to changes in traffic conditions. Problems created by an unwarranted signal, such as excessive delay, increased rerouting of traffic to less-appropriate roads and intersections, higher crash rates, and disobedience of the traffic signal can be addressed by removing the signal if doing so would not create worse problems.

## Slide 26: A7: Remove Unwarranted Signal
Signalized intersections generally experience crashes of different types than unsignalized intersections but not necessarily a lower total crash rate. Converting the intersection to unsignalized may not improve the total crash rate, but it may improve crash severity for some crash types.
Studies should be performed when considering removing a signal, just as installation of a signal is studied. This study should identify the appropriate replacement traffic control devices and any sight distance restrictions that may not have been an issue while under signalized control.
Notes: This option is not explicit in NCHRP 500, but is an important thing to note: you can also remove a warranted signal. The text shown here IS from NCHRP 500

## Slide 27
Most important statement in MUTCD regarding warrants:
The satisfaction of a traffic signal warrant or warrants shall not in itself require the installation of a
traffic control signal.

## Slide 28: Questions?

## Slide 29: Category B – Reduce Frequency and Severity of Intersection Conflicts through Geometric Improvements

## Slide 30: B1: Provide or Improve Left-Turn Channelization
This strategy includes the following:
Providing left-turn lanes,
Lengthening left-turn lanes,
Providing positive offset for left-turn lanes,

## Slide 31: Offset Left-Turn Lanes

## Slide 32: Offset Left-Turn Lanes

## Slide 33: B1: Provide or Improve Left-Turn Channelization
This strategy includes the following:
Providing left-turn lanes,
Lengthening left-turn lanes,
Providing positive offset for left-turn lanes,
Providing positive guidance with channelization, and
Delineating turn path.

## Slide 34: Delineation of Turning Path

## Slide 35: B2: Provide or Improve Right-Turn Channelization
Many collisions at signalized intersections are related to right-turn maneuvers. A key strategy for minimizing such collisions is to provide exclusive right-turn lanes. It is also important to ensure that the right-turn lanes are of sufficient length to allow vehicles to decelerate before turning, ideally without affecting the flow of through traffic. Right-turn lanes remove slow vehicles that are decelerating to turn right from the through-traffic stream, thus reducing the potential for rear-end collisions.
Notes: So here is the rub, right turn lanes increase intersection speeds by getting the decelerating right turning vehicles out of the way of the through vehicles. This is a good thing on a high-speed facility, but if you are trying to do speed management and reduce speeds, right turn lanes may work against you.

## Slide 36: B3: Improve Geometry of Ped and Bike Facilities
Geometric or physical improvements that can be made to an intersection to increase pedestrian safety include the provision of the following:
Continuous sidewalks,
Signed and marked crosswalks,
Sidewalk set-backs,
Median refuge areas,
Physical barriers to restrict pedestrian crossing maneuvers at higher-risk locations
Notes: A few other things to mention:
If you have nighttime ped crashes, intersection lighting.
Relocation of transit stops from the near side to the far side of the intersection
Other traffic calming applications to reduce vehicle speeds or traffic volumes

## Slide 37: B3: Improve Geometry of Ped and Bike Facilities (cont.)
Possible improvement projects for bikes would include the following:
Widening outside through lanes (or adding bike lanes),
Providing median refuge areas,
Providing independent crossing structures,
Upgrading storm drain grates with bicycle-safe designs, and
Implementing lighting.
Notes: Other things to consider:
Green bike lanes
Bike boxes

## Slide 38: B4: Revise Geometry of Complex Intersections
This strategy includes a series of mostly higher-cost solutions:
Converting a four-leg intersection to two T intersections,

## Slide 39: Convert a 4-legged Intersection to Two T Intersections
Notes: If you are going to do this, the T-intersections must be in the right order as shown here. In this case, the left turn storage for both of the T-intersections would be outside of the two intersections. If the connections were reversed, the left turn storage would be constrained by the intersection spacing. That would create operational nightmares. [see next slide]

## Slide 40: Convert a 4-legged Intersection to Two T Intersections
Don’t do it this way!!!

## Slide 41: B4: Revise Geometry of Complex Intersections
This strategy includes a series of mostly higher-cost solutions:
Converting a four-leg intersection to two T intersections,
Converting two T intersections to one four-leg intersection,
Improving intersection skew angle, and
Improving deflection in the through-vehicle travel path.
Closing an intersection leg
Notes: A fifth solution, closing an intersection leg, is one commonly tried when addressing the problem of complex intersections. This can be a low-cost solution because it does not typically require major reconstruction.
However, the overall strategy we should be looking at is to SIMPLIFY. Keep it simple!

## Slide 42: B5: Construct Special Solutions
This strategy includes the following:
Providing indirect left turn,

## Slide 43: Indirect Left Turns
Jug handle
Median U-turn (MUT)
Notes: First is jug handle – popular in NJ. No left turns at the center intersection. Left turns occur via the loop and right turns, or from the side street the left turn is made at the T-intersection.
Second is Median U-Turn (MUT)

## Slide 44: Indirect Left Turns
Indirect Left Turns
Quadrant Intersection
Continuous Flow Intersection
Notes: Third is a Quadrant Intersection
Forth is a Continuous Flow intersection – NOT a fan. Imagine how confusing for unfamiliar drivers or especially peds.

## Slide 45: B5: Construct Special Solutions
This strategy includes the following:
Providing indirect left turn,
Reconstructing intersections, converting signalized intersections to roundabouts,
Convert two-way streets to a one-way pair, and
Constructing interchanges.

## Slide 46: Questions?

## Slide 47: Category C - Improve Sight Distance at Signalized Intersections

## Slide 48: C1: Clear Sight Triangles
Sight distance improvements can often be achieved at relatively low cost by clearing sight triangles to restore sight distance obstructed by vegetation, roadside appurtenances, buildings, bus stations, or other natural or man-made objects.
The most difficult aspect of this strategy is the removal of sight restrictions located on private property. The legal authority of highway agencies to deal with such sight obstructions varies widely, and the time (and possibly the cost) to implement sight distance improvements by clearing obstructions may be longer if those obstructions are located on private property.
Notes: Since sight distance is a greater issue at intersections with stop control than at signalized intersections, more research has been performed on the effectiveness of sight distance improvements at stop-controlled intersections. Not much research has been done for sight distance at signalized intersections.

## Slide 49: C2: Redesign Intersection Approaches
Signalized intersections with sight-distance-related safety problems that cannot be addressed with less expensive methods (such as clearing sight triangles, adjusting signal phasing, or prohibiting turning movements) may require horizontal or vertical (or both) realignment of approaches. Realigning both of the minor-road approaches so that they intersect the major road at a different location, or a different angle, can help address horizontal sight distance issues.
Notes: This is a high-cost, longer-term treatment for the intersection, but if completed according to applicable design policy, it should help alleviate crashes related to sight distance.
There are significant ROW and property access issues involved in this strategy, and public information campaigns are vital to the success of the intersection improvements.
Intersection relocation and closure, elimination of intersection skew, and offsetting of left-turn lanes are all strategies that involve improvements to approach alignment to improve sight distance. These strategies are each covered in greater detail in the unsignalized intersection guide.

## Slide 50: Questions?

## Slide 51: Category D - Improve Driver Awareness of Intersections and Signal Control

## Slide 52: D1: Improve Visibility of Intersections on Approach(es)
This strategy includes the following:
Improving signing and delineation,
Installing larger signs,
Providing intersection lighting,
Installing rumble strips on approaches, and
Installing queue detection system.
Notes: Installing larger signs – great for aging road users
Intersection lighting – best thing for night crashes
Rumble strips – only on rural approaches
Queue detection system – especially effective where queues start to reduce stopping sight distance

## Slide 53: Improving Signing and Delineation
Notes: Advance Street Name Signs

## Slide 54: D2: Improve Visibility of Signals and Signs at Intersections
Visibility of traffic signals and signs at intersections may be obstructed by physical objects (such as signs or other vehicles) or may be obscured by weather conditions, such as fog or bright sunlight. Also, drivers’ attention may be focused on other objects at the intersection, such as extraneous signs. Poor visibility of signs and signals may result in vehicles not being able to stop in time for a signal change or otherwise violating the intended message of a regulatory or directional sign.
Notes: [continues next slide]

## Slide 55: D2: Improve Visibility of Signals and Signs at Intersections
Methods for improving visibility of traffic signals and signs include the following:
Install additional signal head (supplementary head),
Provide visors to shade signal lenses from sunlight,
Install backplates,
Remove or relocate unnecessary signs, and
Provide far-side left-turn signal.

## Slide 56: Questions?

## Slide 57: Category E - Improve Driver Compliance with Traffic Control Devices

## Slide 58: E1: Provide Public Information and Education
Safety problems at signalized intersections cannot always be solved only with engineering countermeasures. Enforcement of traffic regulations or public information campaigns may be the best way to improve intersection safety.
Providing targeted public information and education on safety problems at intersections is a preventive measure that can help improve driver compliance with traffic control devices and traffic laws.

## Slide 59: E2: Provide Targeted Conventional Enforcement of Traffic Laws
Enforcement is a potential countermeasure to unsafe and illegal motorist behavior at intersections. Studies report the reduction of traffic law violations when enforcement is used. Traffic law enforcement agencies will often select locations for targeted enforcement when crash, citation, or other sources of information suggest that the site is unusually hazardous due to illegal driving practices, such as speeding or red-light running.
Notes: Targeted enforcement of traffic laws is a short-term, moderate-cost measure to address site specific signalized intersection safety. Though this is an effective strategy, the effectiveness has often been found to be short-lived. It is difficult—if not impossible—to provide constant enforcement of traffic regulations due to funding and staffing reasons, so periodic enforcement may be necessary to sustain the effectiveness of this strategy.

## Slide 60: E3: Implement Automated Enforcement of Red-Light Running
Automated enforcement refers to the use of photo radar and video camera systems connected to the signal control. Such systems record vehicles proceeding through the intersection after the signal displays red. Red-light-running cameras turn on after the signal turns red. A detector senses approaching vehicles and sends a signal to the camera, which photographs the vehicles as they enter the intersection. It is possible to set a grace period (generally one second) so that the cameras do not photograph people who were caught in the dilemma zone and enter the intersection just after the signal turns red.

## Slide 61: E4: Implement Automated Enforcement of Approach Speeds
Enforcement of traffic regulations is an important part of an overall intersection safety improvement strategy, but limited resources constrain the efforts police can devote to providing speed enforcement. Traffic law enforcement agencies will often select locations for targeted enforcement when crash, situation, or other sources of information suggest that the site is unusually hazardous due to illegal driving practices. Crash types that might indicate speeding as a concern include right-angle and rear-end collisions. Speed-enforcement cameras (also known as photo radar) are a potential method to use in these locations.

## Slide 62: E5: Control Speed on Approaches
Since speed contributes to crash severity, lowering speeds on approaches to intersections can help reduce the severity of crashes. Slowing vehicle speeds on intersection approaches can improve safety for motorists, pedestrians, and bicyclists. Various techniques for attempting to control speeds on approaches involve geometric design, signal control technology, and other traffic calming treatments.
Notes: Things like:
Construction of a horizontal curve on the approach to an intersection; raised intersection; chicanes, speed tables

## Slide 63: Questions?

## Slide 64: Category F - Improve Access Management near Signalized Intersections

## Slide 65: F1: Restrict Access to Properties Using Driveway Closures or Turn Restrictions
Restricting access to commercial properties near intersections by closing driveways on major streets, moving them to cross streets, or restricting turns into and out of driveways will help reduce conflicts between through and turning traffic. Such conflicts can lead to rear-end and angle crashes related to vehicles turning into and out of driveways and speed changes near the intersection and the driveway(s).

## Slide 66: F2: Restrict Cross-Median Access near Intersections
When a median opening on a high-volume street is near a signalized intersection, it may be appropriate to restrict cross-median access for adjacent driveways. For example, left and U-turns can be prohibited from the through traffic stream, and left turns from adjacent driveways can be eliminated. Restrictions can be implemented by signing, by redesign of driveway channelization, or by closing the median access point via raised channelization.
Notes: When access patterns are changed or restricted, the movements restricted in that location should be accommodated at a safe location nearby.

## Slide 67: Category G - Improve Safety through Other Infrastructure Treatments

## Slide 68: G1: Improve Drainage in Intersection and on Approaches
Drainage problems on approaches to and within intersections can contribute to crashes just as they can on roadway sections between intersections. However, within an intersection, the potential for vehicles on cross streets being involved in crashes contributes to the likelihood for severe crashes, specifically angle crashes.
Notes: Drainage issues can be especially problematic for pedestrians and bicyclists. How often do you see silt accumulation in the ADA ramps?

## Slide 69: G2: Provide Skid Resistance in Intersection and on Approaches
The coefficient of friction is most influenced by vehicle speed, vehicle tire condition, and surface condition. Consideration should be given to improving the pavement condition to provide good skid resistance, especially during wet weather. This can be accomplished by:
• Providing adequate drainage,
• Grooving existing pavement, and
• Overlaying existing pavement.

## Slide 70: G3: Coordinate Closely Spaced Signals near at-Grade Railroad Crossings
At-grade railroad crossings on approaches to intersections have potential safety problems related to vehicle queues forming across the railroad tracks. The railroad and nearby traffic control signals should be coordinated to provide preemption of the traffic signals when trains are approaching the intersection.

## Slide 71: G4: Relocate Signal Hardware out of Clear Zone
Traffic signal hardware represents a potential roadside hazard similar to utility poles, trees, and other large fixed objects. Traffic signal supports and controller cabinets should be located as far from the edge of pavement as is possible, especially on high-speed facilities, as long as this does not adversely affect visibility of the signal indications. Consideration should be given to shielding the signal hardware if it cannot be relocated.
The signal hardware should not obstruct sight lines.

## Slide 72: G5: Restrict or Eliminate Parking on Intersection Approaches
Parking adjacent to turning and/or through lanes on intersection approaches may create a hazard. It can cause a frictional effect on the through traffic stream, can often block the sight triangle of stopped vehicles, and may occasionally cause the blocking of traffic lanes as vehicles move into and out of parking spaces. Restricting and/or eliminating parking on intersection approaches can reduce the workload imposed on the driver and limit additional collision opportunities.

## Slide 73: Questions?

## Slide 74
Signalized Intersection Safety Strategies
Notes: This is one of the handouts also. It references the same strategies that we just talked about, but is a good and handy one-page reference. However, print it on 11 x 17.

## Slide 77: Questions?