## Slide 1: District One Traffic Safety Academy
Presented by: Larry Hagen, P.E., PTOE, RSP
Session 1 - Introduction

## Slide 2: Introduction:
What is the Academy
  What to expect
  How it works

## Slide 3: Strategic Highway Safety Plan

## Slide 4: Resources – Strategic Highway Safety Plan (SHSP)
Required of each state by FHWA in order to receive federal safety funds
The SHSP is a statewide, data-driven safety plan for all of Florida’s road users
Identifies 13 “Emphasis Areas”
Emphasis Areas guide the safety efforts
Focus is on fatalities and serious injury crashes

## Slide 6
Notes: Current version is the 2016 version. It is typically updated every 5 years. The 2021 version is currently being worked on.

## Slide 7
Notes: Truly multi-disciplinary. Look at the people that signed off on it here:

## Slide 8: Vision is a Fatality Free Transportation System
So how are we doing in pursuit of that goal?
Notes: Numbers are heading the wrong way.

## Slide 11: Elderly Road Users in Florida
According to the Department of Highway Safety and Motor Vehicles:
There are 1,256,839 licenses for people 65-69 years old
There are 1,862,415 licenses for people 70-79 years old
There are 713,085 licenses for people 80-89 years old
There are 112,148 licenses for people 90+ years old
Notes: Statistics as of January 1, 2020

## Slide 13: Florida’s Transportation System
Note how sparse the bicycle / pedestrian network is on the State Highway System

## Slide 14: State vs Local Roads

## Slide 15: Florida’s Urban Areas
Notes: Remember: 9 out of 10 Floridians live in urbanized areas

## Slide 16
Notes: 13th Emphasis Area – Improve Crash Data (Traffic Records and Information Systems)

## Slide 20
Notes: We now look at specific strategies related to each of the emphasis areas.

## Slide 37: Questions?

## Slide 38: Crash Data Resources

## Slide 39: Fatality Analysis Reporting System
Maintained by NHTSA
National records of fatal crash data
Typically about two years behind
Good historical and trend data

## Slide 40
Notes: From the FARS website, you can select Florida data.

## Slide 41: Crash Analysis Reporting System
Maintained by DHSMV
Statewide database of vehicle crash data
Typically one to two years behind
Summaries only – no crash narratives
Certified crash data that goes to NHTSA

## Slide 42: Signal 4 Analytics
GIS-based crash record management system
Maintained by the University of Florida
Pretty current crash data
Input from state and local sources
Includes link to .PDF of crash report
Charts & graphs to simplify analysis
Export to Excel for further analysis
Notes: Can also do rough high-level analysis similar to CARS. But NOT the certified numbers.

## Slide 45
Notes: You can click on any of the dots here to see more information about that particular crash, including the crash number, with a hot-link to the crash report.

## Slide 47: Crash Countermeasure Resources

## Slide 48: FHWA’s Proven Safety Countermeasures
www.safety.fhwa.dot.gov/provencountermeasures

## Slide 49
Notes: 20 proven countermeasures. On the FHWA website, you can click on any of these icons to find out more about these specific countermeasures.

## Slide 50: FHWA Intersection Safety Strategies
Notes: FHWA Intersection Safety Strategies Brochure

## Slide 51: FHWA Intersection Safety Strategies
Notes: FHWA Intersection Safety Strategies Brochure

## Slide 52: Crash Modification Factors Clearinghouse
www.cmfclearinghouse.org

## Slide 54
Notes: I searched for “flashing yellow arrow.” It returned 38 CMFs: 2 under Traffic Control Type, 36 under Signal Phasing or Timing.

## Slide 55
Notes: Here, I searched for LPI = Leading Pedestrian Interval. 19 CMFs were found for LPI. Look at the first five of the 19 here.

## Slide 56
Notes: Here are more of the CMFs for putting in a LPI. The values range from 0.72 to 1.09 for all crashes, and 0.413 to 0.91 for vehicle/ped crashes. That means between 28% crash reduction and 9% crash increase for all crashes; and a 9% to 58.7% reduction in veh/ped crashes. That is a pretty wide range! Which one do you use? That is a topic we will look at in a later session.

## Slide 57
Notes: FHWA’s Desktop Reference for Crash Reduction Factors

## Slide 60
Notes: Note all the different CRFs for improving the change intervals. Note for older drivers; 42% CRF! Need to note that ITE recently update the recommended practice.

## Slide 61
Notes: Note 70% reduction in emergency vehicle crashes by using preemption. Look at all of the ped signal CMFs!

## Slide 62
Notes: Note that LPI only has 5% CRF here. Actuation of a signal has 80% CRF for left turn crashes?

## Slide 63: Questions?

## Slide 64: Why are we doing this?

## Slide 65: We all have families / loved ones that use the roads
Notes: Sometimes in our vehicles…

## Slide 66: We all have families / loved ones that use the roads
Notes: Sometimes as pedestrians.

## Slide 67: We all have families / loved ones that use the roads
Notes: Sometimes as pedestrians.

## Slide 68: We all have families / loved ones that use the roads
Notes: Sometimes as pedestrians.

## Slide 69: Vision Zero – A New Vision for Safety
Notes: We will talk in another session about the Safe Systems approach and what it means and where it could take us.

## Slide 70: Taking the Lead for Safe Streets
Vision Zero is not a slogan, not a tagline, not even just a program. It is a fundamentally different way to approach traffic safety.

## Slide 71: Questions?
Notes: Go to www.trafficsafetyguru.com/safetyacademy

## Slide 72: Thank you for attending today’s session!
Notes: In our next session, we will be talking about safety treatments. It will be on Monday, the 19th at 10AM.